## Slide 1: KJM 3110 Electrochemistry Chapter 4. Electrosynthesis

## Slide 2: Recap exercise from Ch. 3 Electrochemical cells
Take the lead-acid cell as example.
What is the situation, driving force(s), and processes going on in each of the following cases:
Standard state. (a1 = a2 = a3 … = Q = 1)
  Open circuit.
  Short circuit.
Actual lead-acid battery
  Overall equilibrium (OCV = 0)
  Local electrode equilibrium
    I = 0 (OCV = ?)
  Galvanic operation
    I > 0
  Electrolytic operation
    I < 0

## Slide 3: Recap from Ch. 3 Electrochemical cells - Summary
Equilibrium
  I = 0
Galvanic operation
  I > 0
Electrolytic operation
  I < 0

## Slide 4: Ch. 4 - Electrosynthesis
Many materials and chemicals can be fabricated most efficiently by electrolysis – electrosynthesis.
For many, it is the only known way.
  Electrowinning from ore
  Exclusive: Li, Na, K, Mg, Ca, Sr, Ba, Ra, Al, Ta (+ F2, Cl2)
  Competitive: Cr, Mn, Co, Ni, Cu, Ag, Au, Zn, Cd, Ga, In, Tl
In this chapter we familiarize ourselves with such processes.
This will make us understand further the importance of electrochemistry
and strengthen our understanding of electrolytic cells and processes

## Slide 5: Metal production – example: Al by Hall-Hèrault
Al2O3 dissolved in melt of cryolite Na3AlF6 (+CaF2):
Al2O3 + 8F- = 2AlF4- + 3O2- |2
|4
|3

## Slide 6: Chloralkali industry
NaCl(aq) + electricity
Products are Cl2 and H2 and OH-
OH- (NaOH) recycled
Role of membrane?
Many further products
  OCl-, ClO3-, ClO4-
Check equations 4.6-4.11

## Slide 7: Organic electrosynthetic chemistry
Relatively new field of electrochemistry
Nylon
  Hydrogenation step on Cd electrode; acrylonitride to adiponitrile

## Slide 8: Electrolysis of water
ΔG0 = 474.2 kJ/mol E0 = 1.229 V

## Slide 9: Electrolysis of water - negatrode
Hg, Ag, Pb, Cu, Fe:
Mo, W, Ti, Ta:
Pd, Rh, Ir:
Negatrode

## Slide 10: Electrolysis of water - positrode
Metals
  suggested steps, via HO. (or OH.) radicals:
Electrolysis can also be done in alkaline electrolyser to produce H2 and O2
Alternative catalysts can produce intermediate peroxy species at one or both electrodes, e.g.
Negatrode
Positrode

## Slide 11: Alkaline (OH-) and PEM (H3O+) electrolysers
NEL (Norway) one of the World’s leading suppliers
  Originated from Norsk Hydro’s electrolysers for ammonia production
  Product line: https://nelhydrogen.com/water-electrolysers-hydrogen-generators/
Medium sized to large alkaline electrolysers
Small to medium sized PEM electrolysers

## Slide 12: Steam electrolysis
Norway has expertise in solid-state high-temperature (ceramic) electrolytes
Enables electrolysis of steam rather than liquid water
Thermodynamically more beneficial if steam and/or heat is free and available
Main features of PEM, proton ceramic, and solid oxide electrolysers:
Vøllestad, E. et al., Nature Materials 2019

## Slide 13: Heat balance of electrochemical processes; Steam electrolysis
ΔHreact + q + wel = ΔHprod
H2O = H2 + ½ O2
H2O(g) = H2(g) + ½ O2(g)
H2O(l) = H2(g) + ½ O2(g)
Electrical efficiency:
fel = wel/(ΔHprod - ΔHreact)
At q=0: wel = ΔGr and fel = ΔGr /ΔHr
= (ΔHr – TΔSr)/ΔHr = 1 – TΔSr/ΔHr
Faradaic efficiency ff = ratio of product rate over current
Total efficiency ft = fel * ff
Electrochemical cell
ΔHreact
ΔHprod
wel
q
q = 0: Thermoneutral

## Slide 14: Exercise
In the previous slide, what contributes to the heat exchange q?
At thermoneutral operation, q = 0. Express this situation with words.
Why – qualitatively – is steam electrolysis thermodynamically better than water electrolysis?

## Slide 15: 3 unique technologies by proton ceramics for H2
Steam electrolysis & compressor
  2H2O = O2 + 2H2
      Duan, C. et al., Nature Energy 2019
      Vøllestad, E. et al., Nature Materials 2019
Methane dehydroaromatization (MDA); GTL
  6CH4 = C6H6 + 9H2
      Morejudo, S. et al., Science 2016
Proton membrane reforming (PMR)
  CH4 + 2H2O = CO2 + 4H2
      Malerød-Fjeld, H. et al., Nature Energy 2017
U
CO2
CH4+2H2O
8H+
4H2
U
8H+
C6H6
6CH4
9H2

## Slide 16: CO2 utilisation hype: CO2 + H2O co-electrolysis
Zhang et al. describes co-electrolysis using O2- or H+ conducting high-temperature solid-state electrolytes
One produces dry, the other wet synthesis gas (CO + H2)
X. Zhang et al., J. Energy Chemistry, 26 [5] (2017), 839-853

## Slide 17: Exercise
What is syngas, and what is it used for?
In the previous slide, the O2- ion conductor provides a better process than the H+ conductor, because the syngas is preferably dry
Can the H+ conducting cell be improved by a different stoichiometry (mix) of the reactants?
Can a material with mixed O2- and H+ conduction be used as electrolyte? Sketch its operation.
Check out https://www.youtube.com/watch?v=Y2DUMJMba2E&feature=youtu.be

## Slide 18: Use of ion-selective membranes; Electrodialysis Example: NaCl solution inflow split in denuded and concentrated outflows

## Slide 19: Salt splitting with various ion-selective membranes H2 and O2 evolved as byproducts. Example Na2SO4

## Slide 20: Salt splitting with bipolar membranes Salt + Water becomes Acid + Base NaCl(aq) + H2O = HCl(aq) + NaOH(aq)

## Slide 21: Ch. 4 Electrosynthesis - Summary
We have seen some industrial examples of electrolytic operation of electrochemical cells for production of high-energy fuels and chemicals
  Some important
    Hall-Hèrault for aluminium
    Chlor-alkali for chlorine products
    Electrolysis for H2
  Some new trends
    Organic electrosynthesis
Applications of high-temperature solid electrolytes pursued at UiO
Ion-selective membranes give additional possibilities
In electrosynthesis, otherwise impossible reactions become possible
  The electronic energy adds to or – more typically – overpowers the chemical energy
    Thermodynamic
    Kinetic (can also give unique selectivities)
“Control chemistry by controlling electrons”