## Slide 1: KJM 3110 Electrochemistry Chapter 5. Electrochemical power

## Slide 2: Electrochemical power
Previous chapter: Electrical energy to chemical (Gibbs) energy
  Electrolysis
  Charging battery
    Secondary cells; Accumulators, rechargeable batteries)
This chapter: Chemical (Gibbs) energy to electrical energy
  Fuel cell
  Discharging battery
    Primary cells
    Secondary cells; Accumulators, rechargeable battery

## Slide 3: Recap from Ch. 4 Electrosynthesis - Summary
We have seen some industrial examples of electrolytic operation of electrochemical cells for production of high-energy fuels and chemicals
  Some important
    Hall-Hèrault for aluminium
    Chlor-alkali for chlorine products
    Electrolysis for H2
  Some new trends
    Organic electrosynthesis
Applications of high-temperature solid electrolytes pursued at UiO
Ion-selective membranes give additional possibilities
In electrosynthesis, otherwise impossible reactions become possible
  The electronic energy adds to or – more typically – overpowers the chemical energy
    Thermodynamic
    Kinetic (can also give unique selectivities)
“Control chemistry by controlling electrons”

## Slide 4: Batteries
Positive and negative electrodes
Positrode and negatrode
Cathode and anode
Nominal voltage
  = OCV fully charged
Cut-off voltage
Where is the null voltage?
Capacity (amount of charge)
  Coulomb, C. Or A s
  C = A s
  1 A h = 3600 A s = 3600 C
Energy
  Unit?
  Energy density
Power
  Unit?
  Power density

## Slide 5: Storage
Battery: Chemistry
Ultracapacitor: Chemistry + electrode interface
Supercapacitor: Electrode interface
Capacitor: Dielectric

## Slide 6: Lead acid battery

## Slide 7: Primary batteries
Volta pile
Daniell cell
Leclanché wet cell with NH4Cl(aq)
Dry cell
  NH4Cl + ZnCl2 paste
  C powder composite cathode

## Slide 8: Alkaline batteries
In some ways an inversed design…
Other alkaline positrodes
Air battery

## Slide 9: Secondary (rechargeable) batteries (accumulators)
Most widespread: Lead-acid battery.
Repeat from Ch. 3:

## Slide 10: Lead acid batteries: Extraneous reactions
In modern, sealed batteries, diffusion of O2 + reaction 5.24 replenishes the water.

## Slide 11: Li-ion batteries
May be represented simple
or more realistic
Copyright 2013, ACS
The electrolyte used in most lithium-ion cells is a solution of LiClO4 or LiAsF6 in organic carbonates, absorbed in microporous polyolefin separator.

## Slide 12: Na-S battery
Exercise: What is the total reaction and Gibbs expression?

## Slide 13: Fuel cells; continuous supply of fuel and oxidant air
Fuels:
  H2
  Reformed CH3OH
  Reformed CH4
Electrolytes:
  Alkaline
  Acid (Phosphoric acid and PEM)
  Molten carbonate
  Solid oxide
  Proton ceramic

## Slide 14: Heat balance of electrochemical processes; Fuel cell
ΔHreact + q + wel = ΔHprod
H2 + ½ O2 = H2O
H2(g) + ½ O2(g) = H2O(g)
(Lower heating value)
H2(g) + ½ O2(g) = H2O(l)
(Higher heating value)
Electrical efficiency:
fel = wel/(ΔHprod - ΔHreact)
wel = ΔGr and fel = ΔGr /ΔHr
= (ΔHr – TΔSr)/ΔHr = 1 – TΔSr/ΔHr
Electrical efficiency depends on whether one uses LHV or HHV
Faradaic efficiency ff = Current over fuel used.
Fuel utilisation fu = fuel spent over total fuel supplied (unspent fuel may be recirculated or afterburnt).
Total efficiency ft = fel * ff *fu
Electrochemical cell
ΔHreact
ΔHprod
wel
q

## Slide 15: Redox flow battery
What are the electrodes?
What goes on in the membrane?

## Slide 16: Ch. 5 Summary
Exercise for the class: Discuss each sentence, not least the last one. When was this written?