## Slide 1: KJM 3110 Electrochemistry Chapter 15 Electrochemistry with Periodic Signals
Most figures from the textbook we use for the course, via its web resources:

## Slide 2: Ch. 14 Other interfaces - Summary

## Slide 3: AC voltage and current. Impedance and power.
AC voltage
the amplitude can be expressed as
  Amplitude U0
  Peak-to-peak voltage, Up-p = 2U0
  Root mean square (rms) voltage
  Urms = U0/2 = Up-p/(22)
Resulting AC current can have a different amplitude and phase angle as a result of the impedance:
Impedance Z* = U* / I*
Instantaneous power P = U* I*
Power integrated over time:

## Slide 4: Textbook’s introduction to periodicity
Direct current (DC) vs alternating current (AC)
Sinusoidal case:
Angular frequency is ω = 2πf
Phase angle φ
What is the periodicity P here?

## Slide 5: Conductivity cell
Conductivity of the electrolyte
Calibrate the geometrical factors by using a 1 M KCl solution
AC measurement: Current
Will generate voltages over an electrochemical cell
over R:
over C:
Phase shifts? Amplitude ratios?

## Slide 6: Faradaic effects of AC Impedance, harmonics, rectification
The treatment that follows aims to show that there are two contributions to electrode impedance: Kinetics and transport
Apply AC current, measure AC voltage, or vice versa
Impedance Z (equivalent to resistance R in DC)
Faradaic effects
  Apply (small) AC voltage
  Reaction
  Response on concentrations

## Slide 7: Faradaic effects of AC Impedance, harmonics, rectification
Oscillating current changes the concentrations of reactants and products
Semi-integration yields
The product and reactant concentrations are shifted -45° and +135°, respectively, i.e., 180° apart.
Total concentration close to constant
Semi-integration is not curriculum, but leads to concentrations ±π/4 out of phase

## Slide 8: Relation to voltage – Butler-Volmer
From Ch. 7, a version of the Butler-Volmer equation:
Charge transfer resistance Rct in phase
Warburg element W
(transmission line) R/C = W2 out of phase

## Slide 9: The RctW impedance

## Slide 10: The Warburg impedance
W (unit of ohm s-1/2)
Reflects a combination of
  Diffusion
  Chemical capacitance
Appears in AC circuits to represent the impedance of mass transport
  In series with the charge transfer resistance
Imposes a complex impedance ZW(ohm) = W/√(2ω) - jW/√(2ω)
Has a constant, frequency independent phase shift of –π/4 (-45°)

## Slide 11: Reversibility index λ
What we have done here is to perturb a reaction which reacts with kinetic and mass transport limitations (Rct and W, respectively)
Reversible: Rct very small, λ >> 1
Quasireversible λ ≈ 1
Irreversible: Rct large, λ << 1. No faradaic periodicity.
Reversibility index for AC impedance

## Slide 12: AC impedance measurement
Electrochemical impedance spectroscopy (EIS)
Impedance spectrometer (frequency response analysers)
  E.g. Solartron SI 1260 FRA
  0-3 V rms AC 0.01 mHz – 32 MHz, -42 - +42 V DC
Electrode electrical elements
  Ru uncompensated electrolyte resistance (ohmic)
  Rct charge transfer resistance (kinetics)
  W Warburg impedance (diffusion)
  C Capacitance (double layers)

## Slide 13: Deviations from ideality at large perturbations
Small perturbations, linear range (blue)
  Near-ideal response
Larger perturbations, non-linear range (red)
  Non-ideal response
  Rectification
  Harmonics
    Response contains features sharper (of frequencies higher) than the perturbation frequency
    Overharmonics (integer multiple of perturbation frequency)

## Slide 14: AC impedance representations
Impedance has magnitude but also contains a phase angle between E and I
Vector in 2-dimensional Z space
In-phase and out-of-phase components
Real part Z’
Imaginary part jZ’’
Z = Z’ + jZ’’ or Z* = Z’ + jZ’’ Complex numbers j =√-1 or j2 = -1
The value of Z – often denoted |Z| – is the length of the vector:
|Z| = √(Z2) = √(Z’2+Z’’2) = √(Z’2–(jZ’’)2) = √((Z’+jZ’’)(Z’-jZ’’))
Z’
Z’’
Complex conjugate

## Slide 15: Complex impedance Z* and admittance Y*
Z* = U*/I* = Z/ + jZ// = R + jX
  Z* Complex impedance
  |Z| Impedance
  R Resistance
  X Reactance
Y* = 1/Z* = I*/U* = Y/ + jY// = G + jB
  Y* Complex admittance
  |Y| Admittance
  G Conductance
  B Susceptance

## Slide 16: Impedance and admittance of discrete elements
Series RCL
Z* = Z/ + jZ// = R + jX
Parallel (RCL)
Y* = Y/ + jY// = G + jB
Resonance for (RC) when G = ωC or C=G/ω or ω=1/(RC)

## Slide 17: Y*=1/Z* and Z*=1/Y*

## Slide 18: Randles-Erschler circuit
Ru(C(RctW))

## Slide 19: Equivalent circuit of a simple electrochemical cell
Ls series inductance
Relectrolyte
Cgeom
Rct charge transfer resistance
Cdl double layer capacitance
Rmt mass transfer resistance
Cch chemical capacitance
Ls series inductance
Relectrolyte
Cgeom
Rct charge transfer resistance
Qdl double layer capacitance constant phase element (CPE)
Rmt mass transfer resistance
W Warburg impedance: CPE with 45° phase angle
Ls
Relectrolyte
Rct
Rmt
Cgeom
Cdl
Cch
Ls
Relectrolyte
Rct
Rmt
Cgeom
Qdl
W

## Slide 20: Build the circuit impedance
Add Rct and W in series, real and imaginary parts separate:
Add C in parallel:

## Slide 21: Build the circuit impedance
Add Ru in series (has only real part):

## Slide 22: Deconvolute and parameterise the circuit
Low frequencies

## Slide 23: «Impedance plots»
Imaginary part Z’’ vs real part Z’
Or often –Z’’ vs Z’
Argand diagram
Sluyters plot
Cole-Cole plot
Nyquist plot
Reversible, Rct negligible
Harry Nyquist
1889-1976

## Slide 24: The Z semicircle: (RC)
Irreversible
Fast diffusion; W is negligible
Ru(RctC)
Forms a semicircle distanced from origo
Case dominated by only W shown as a straight line
Case with all components significant over a large frequency range
Frequency is a so-called dependent variable

## Slide 25: Constant phase elements (CPE)
Constant phase elements (CPE); symbol Q
Mathematically mimics the impedance of real, non-ideal, processes and components; dispersions in time constants
Q has admittance
and, by inversion, impedance
where Z0 = 1/Y0
n = 1 Capacitor
n = 0 Conductor/Resistor
n = -1 Inductance
n = 0.5 Warburg element
Values in between: Intermediate behaviours

## Slide 26: Circuit elements overview table

## Slide 27: AC voltammetry (qualitative approach only)
«Discriminating against capacitive current»
Superimpose typically 10 mV AC on e.g. +/- 150 mV DC voltammogram
AC current response to AC voltage perturbation
  In-phase with voltage is faradaic
  Out-of-phase is capacitive

## Slide 28: Fourier transform voltammetry
Not curriculum
Fourier transforms convert between frequency and time domains
Example:
An impedance spectrum reflects a circuit’s transient current-voltage relationships in the frequency domain
In the current interruption technique, we polarise the circuit to steady state current, then interrupt it so that current is zero while the voltage decays from all capacitances over the respective resistors. The decay curve contain all the same information, from high to low frequencies, as the impedance spectrum.
One can generate the other and vice versa by Fourier transforms.

## Slide 29: Summary Ch. 15 Electrochemistry with Periodic Signals